## Slide 1: 8-bit ALU VLSI Design with 16 choices IC
  Presented by : Soumyadeep Mukherjee, Subhadip Hait, Rup Mondal, Suman Bera, Subhodeep Ghosh, Subhadeep Jana

## Slide 2: Introduction to ALU
Arithmetic Logic Unit (ALU) is the computational core of a digital processor.
It performs arithmetic operations like addition and subtraction and logical operations like AND, OR and XOR.
An 8-bit ALU processes 8-bit binary data and produces 8-bit output.
It works according to control signals generated by control unit.

## Slide 3: Working Principle
The ALU takes two 8-bit inputs A and B.
A 4-bit control signal selects one operation among 16 operations.
Arithmetic block performs addition and subtraction.
Logic block performs logical operations.
Shift block performs shift operations.
Multiplexer selects final output.

## Slide 4: DATATYPE REQUIREMENT
Inputs may be declared as STD_LOGIC_VECTOR.
For arithmetic operations, converted to unsigned.
Multiplication and division work only on unsigned, signed, or integer types.
Shifter Circuit performs bit shifting.
Multiplexer selects required output.
Flags Generated:
Carry Flag
Zero Flag

## Slide 5: 16 Operations of ALU
0000 ADD
0001 SUB
0010 MUL
0011 DIV
0100 AND
0101 OR
0110 XOR
0111 NOT
1000 NAND
1001 NOR
1010 XNOR
1011 INC
1100 DEC
1101 SHL
1110 SHR
1111 PASS

## Slide 6: DESIGN REQUIREMENTS
Used case statement for operation selection.
Used combinational process block.
Convert final result back to STD_LOGIC_VECTOR.
Ensure code synthesizable.

## Slide 7: LIBRARIES AND REQUIREMENTS
ALU SPECIFICATIONS
Input A = 8 bits
Input B = 8 bits
Select line S = 4 bits
Output y = 8 bits
MANDATORY LIBRARIES
Library IEEE;
Use IEEE.STD_LOGIC_1164.ALL;
Use IEEE.NUMERIC_STD.ALL;

## Slide 8: Applications
Applications:
Microprocessors
Microcontrollers
DSP Systems
Digital Electronics
The designed 8-bit ALU performs 16 operations efficiently.
It demonstrates basic VLSI design concepts.
The design can be extended to 16-bit and 32-bit ALU.

## Slide 9: Conclusion
The 8-bit Arithmetic Logic Unit (ALU) was successfully designed to perform 16 arithmetic, logical, shift, and data transfer operations using digital design principles. The ALU processes two 8-bit inputs and produces an 8-bit output based on control signals, demonstrating the fundamental operation of a processor's computation unit.
This project helped in understanding the architecture of ALU, control signal operation, and VLSI design concepts such as modular design, speed optimization, and efficient hardware utilization. The design shows how complex processor operations can be implemented using simple digital building blocks.

## Slide 10: THANK YOU ANY QUESTIONS?